## Slide 1: Dual Link Image Coding for Earth Observation Satellites
Francesc Aulí-Llinàs
Dep. of Information and Communications Engineering,
Universitat Autònoma de Barcelona, Spain

## Slide 2
TABLE OF CONTENTS
INTRODUCTION
EXPERIMENTAL RESULTS
DUAL LINK IMAGE CODING
CONCLUSIONS
Earth Obervation (EO) satellites in geosynchronous orbits have limited download capacity
Imaging sensors in EO satellites have increased their resolution
Need to trim down data before it is downloaded
Research purpose: increase the download capacity of EO satellites
  Motivation

## Slide 3
Earth Obervation (EO) satellites in geosynchronous orbits have limited download capacity
Imaging sensors in EO satellites have increased their resolution
Need to trim down data before it is downloaded
Research purpose: increase the download capacity of EO satellites
  Motivation
CONCLUSIONS
TABLE OF CONTENTS
INTRODUCTION
DUAL LINK IMAGE CODING
EXPERIMENTAL RESULTS

## Slide 4
INTRODUCTION
1
SATELLITES’ ORBITS

## Slide 5
INTRODUCTION
1
SATELLITES’ ORBITS
  GEOSYNCHRONOUS
    Located upon a stationary
    point on the Earth’s equator
    High altitudes: 22,000 miles
    Ground stations with
    uninterrupted line of sight
    Employed for:
    Communications
    TV broadcast
    Weather monitoring
    …

## Slide 6
INTRODUCTION
1
SATELLITES’ ORBITS
  GEOSYNCHRONOUS
    Located upon a stationary
    point on the Earth’s equator
    High altitudes: 22,000 miles
    Ground stations with
    uninterrupted line of sight
    Employed for:
    Communications
    TV broadcast
    Weather monitoring
    …
    PERMANENT COMMUNICATION LINK
    all acquired data can be downloaded

## Slide 7
INTRODUCTION
1
SATELLITES’ ORBITS
  GEOSYNCHRONOUS
    Located upon a stationary
    point on the Earth’s equator
    High altitudes: 22,000 miles
    Ground stations with
    uninterrupted line of sight
    Employed for:
    Communications
    TV broadcast
    Weather monitoring
    …

## Slide 8
INTRODUCTION
2
SATELLITES’ ORBITS
  POLAR
    Revolutions from the North
    to the South Pole
    Low/medium altitudes:
    100 to 10,000 miles
    Ground stations at the poles
    (10-20 minutes for data
    downloading)
    Employed for:
    Earth Observation (EO)
    Surface and atmosphere
    monitoring
    …

## Slide 9
INTRODUCTION
2
SATELLITES’ ORBITS
  POLAR
    Revolutions from the North
    to the South Pole
    Low/medium altitudes:
    100 to 10,000 miles
    Ground stations at the poles
    (10-20 minutes for data
    downloading)
    Employed for:
    Earth Observation (EO)
    Surface and atmosphere
    monitoring
    …
    INTERMITENT COMMUNICATION LINK
    data acquired by high resolution
    imaging sensors may not be fully
    downloaded
RESEARCH PURPOSE:
ENHANCE THE ABILITY OF EO SATELLITES
TO DOWNLOAD THE DATA ACQUIRED BY
THEIR IMAGING SENSORS

## Slide 10
Earth Obervation (EO) satellites in geosynchronous orbits have limited download capacity
Imaging sensors in EO satellites have increased their resolution
Need to trim down data before it is downloaded
Research purpose: increase the download capacity of EO satellites
  Motivation
CONCLUSIONS
TABLE OF CONTENTS
INTRODUCTION
DUAL LINK IMAGE CODING
EXPERIMENTAL RESULTS

## Slide 11
DUAL LINK IMAGE CODING
3
TRADITIONAL APPROACH

## Slide 12
DUAL LINK IMAGE CODING
3
TRADITIONAL APPROACH
  CODING STEPS
    The sensor captures the image

## Slide 13
DUAL LINK IMAGE CODING
3
TRADITIONAL APPROACH
  CODING STEPS
    The sensor captures the image
    The satellite codes the image

## Slide 14
DUAL LINK IMAGE CODING
3
TRADITIONAL APPROACH
  CODING STEPS
    The sensor captures the image
    The satellite codes the image
    The image is transmitted via the downlink

## Slide 15
DUAL LINK IMAGE CODING
3
TRADITIONAL APPROACH
  CODING STEPS
    The sensor captures the image
    The satellite codes the image
    The image is transmitted via the downlink

## Slide 16
DUAL LINK IMAGE CODING
4
TRADITIONAL APPROACH
  CODING STEPS
    The sensor captures the image
    The satellite codes the image
    The image is transmitted via the downlink
  EMPLOYED CHANNEL: downlink only
  (uplink idle most of the time)

## Slide 17
DUAL LINK IMAGE CODING
4
TRADITIONAL APPROACH
  CODING STEPS
    The sensor captures the image
    The satellite codes the image
    The image is transmitted via the downlink
  TYPES OF REDUNDANCY EXPLOITED
    Spatial redundancy
  EMPLOYED CHANNEL: uplink only
  (downlink idle most of the time)

## Slide 18
DUAL LINK IMAGE CODING
4
TRADITIONAL APPROACH
  CODING STEPS
    The sensor captures the image
    The satellite codes the image
    The image is transmitted via the downlink
  TYPES OF REDUNDANCY EXPLOITED
    Spatial redundancy
    Spectral redundancy
  EMPLOYED CHANNEL: uplink only
  (downlink idle most of the time)

## Slide 19
DUAL LINK IMAGE CODING
4
TRADITIONAL APPROACH
  CODING STEPS
    The sensor captures the image
    The satellite codes the image
    The image is transmitted via the downlink
  TYPES OF REDUNDANCY EXPLOITED
    Spatial redundancy
    Spectral redundancy
  EMPLOYED CHANNEL: uplink only
  (downlink idle most of the time)
  LANDSAT 8 SATELLITE
  650 images per day
  352 MB per image
  Repeat cycle: 16 days
  images of an area of
  Barcelona over a period
  of a year

## Slide 20
DUAL LINK IMAGE CODING
4
TRADITIONAL APPROACH
  CODING STEPS
    The sensor captures the image
    The satellite codes the image
    The image is transmitted via the downlink
  TYPES OF REDUNDANCY EXPLOITED
    Spatial redundancy
    Spectral redundancy
  EMPLOYED CHANNEL: uplink only
  (downlink idle most of the time)
  LANDSAT 8 SATELLITE
  650 images per day
  352 MB per image
  Repeat cycle: 16 days
  images of an area of
  Barcelona over a period
  of a year

## Slide 21
DUAL LINK IMAGE CODING
5
TRADITIONAL APPROACH
  CODING STEPS
    The sensor captures the image
    The satellite codes the image
    The image is transmitted via the downlink
  TYPES OF REDUNDANCY EXPLOITED
    Spatial redundancy
    Spectral redundancy
  EMPLOYED CHANNEL: uplink only
  (downlink idle most of the time)
  LANDSAT 8 SATELLITE
  650 images per day
  352 MB per image
  Repeat cycle: 16 days
  images of an area of
  Barcelona over a period
  of a year

## Slide 22
DUAL LINK IMAGE CODING
5
TRADITIONAL APPROACH
  CODING STEPS
    The sensor captures the image
    The satellite codes the image
    The image is transmitted via the downlink
  TYPES OF REDUNDANCY EXPLOITED
    Spatial redundancy
    Spectral redundancy
    Temporal redundancy
  EMPLOYED CHANNEL: uplink only
  (downlink idle most of the time)
  LANDSAT 8 SATELLITE
  650 images per day
  352 MB per image
  Repeat cycle: 16 days
  images of an area of
  Barcelona over a period
  of a year
  satellite’s constraints
  (space, computation & power)

## Slide 23
DUAL LINK IMAGE CODING
5
TRADITIONAL APPROACH
  CODING STEPS
    The sensor captures the image
    The satellite codes the image
    The image is transmitted via the downlink
  TYPES OF REDUNDANCY EXPLOITED
    Spatial redundancy
    Spectral redundancy
    Temporal redundancy
  EMPLOYED CHANNEL: uplink only
  (downlink idle most of the time)
  LANDSAT 8 SATELLITE
  650 images per day
  352 MB per image
  Repeat cycle: 16 days
  images of an area of
  Barcelona over a period
  of a year
  satellite’s constraints
  (space, computation & power)
INSIGHT OF DUAL LINK IMAGE CODING:
SEND REFERENCE INFORMATION VIA THE UPLINK SO THAT TEMPORAL REDUNDANCY
IS ALSO EXPLOITED IN THE SATELLITE

## Slide 24
DUAL LINK IMAGE CODING
6
PROPOSED APPROACH
  CODING STEPS
    The ground station generates and codes
    an estimate image

## Slide 25
DUAL LINK IMAGE CODING
6
PROPOSED APPROACH
  CODING STEPS
    The ground station generates and codes
    an estimate image

## Slide 26
DUAL LINK IMAGE CODING
6
PROPOSED APPROACH
  CODING STEPS
    The ground station generates and codes
    an estimate image
    The estimate is transmitted via the uplink
    and decoded by the satellite

## Slide 27
DUAL LINK IMAGE CODING
6
PROPOSED APPROACH
  CODING STEPS
    The ground station generates and codes
    an estimate image
    The estimate is transmitted via the uplink
    and decoded by the satellite
    The satellite codes the captured image
    using the estimate

## Slide 28
DUAL LINK IMAGE CODING
6
PROPOSED APPROACH
  CODING STEPS
    The ground station generates and codes
    an estimate image
    The estimate is transmitted via the uplink
    and decoded by the satellite
    The satellite codes the captured image
    using the estimate
    The codestream is transmitted via the
    downlink

## Slide 29
DUAL LINK IMAGE CODING
6
PROPOSED APPROACH
  CODING STEPS
    The ground station generates and codes
    an estimate image
    The estimate is transmitted via the uplink
    and decoded by the satellite
    The satellite codes the captured image
    using the estimate
    The codestream is transmitted via the
    downlink
    The ground station decodes the codestream
    and recovers the captured image

## Slide 30
DUAL LINK IMAGE CODING
7
OTHER ASPECTS
  CODING STEPS
    The ground station generates and codes
    an estimate image
    The estimate is transmitted via the uplink
    and decoded by the satellite
    The satellite codes the captured image
    using the estimate
    The codestream is transmitted via the
    downlink
    The ground station decodes the codestream
    and recovers the captured image
  GENERATION OF THE ESTIMATE & RESIDUAL
    The ground station has all captured data
    and vast computational resources to
    generate the estimate
    The satellite must utilize simple techniques
    to exploit the estimate (herein, Y – X = R)

## Slide 31
DUAL LINK IMAGE CODING
7
OTHER ASPECTS
  CODING STEPS
    The ground station generates and codes
    an estimate image
    The estimate is transmitted via the uplink
    and decoded by the satellite
    The satellite codes the captured image
    using the estimate
    The codestream is transmitted via the
    downlink
    The ground station decodes the codestream
    and recovers the captured image
  GENERATION OF THE ESTIMATE & RESIDUAL
    The ground station has all captured data
    and vast computational resources to
    generate the estimate
    The satellite must utilize simple techniques
    to exploit the estimate (herein, Y – X = R)
  SYNCHRONIZATION
    Up/down transmission occurs in parallel,
    so the packets of data must be synchronized

## Slide 32
DUAL LINK IMAGE CODING
7
OTHER ASPECTS
  CODING STEPS
    The ground station generates and codes
    an estimate image
    The estimate is transmitted via the uplink
    and decoded by the satellite
    The satellite codes the captured image
    using the estimate
    The codestream is transmitted via the
    downlink
    The ground station decodes the codestream
    and recovers the captured image
  GENERATION OF THE ESTIMATE & RESIDUAL
    The ground station has all captured data
    and vast computational resources to
    generate the estimate
    The satellite must utilize simple techniques
    to exploit the estimate (herein, Y – X = R)
  SYNCHRONIZATION
    Up/down transmission occurs in parallel,
    so the data packets must be synchronized

## Slide 33
Earth Obervation (EO) satellites in geosynchronous orbits have limited download capacity
Imaging sensors in EO satellites have increased their resolution
Need to trim down data before it is downloaded
Research purpose: increase the download capacity of EO satellites
  Motivation
CONCLUSIONS
TABLE OF CONTENTS
INTRODUCTION
DUAL LINK IMAGE CODING
EXPERIMENTAL RESULTS

## Slide 34
8
EXPERIMENTAL RESULTS
CORPORA OF IMAGES
LANDSAT 8
Alicante (Spain) - WRS-2 path 199, row 33
2048x2048, 11 components, 16 bps
June 23, 2015
LANDSAT 8
Cartagena (Spain) - WRS-2 path 199, row 34
2048x2048, 11 components, 16 bps
February 12, 2014
ESTIMATE
(previous image)
ESTIMATE
(previous image)

## Slide 35
9
LOSSLESS COMPRESSION (entropy-based evaluation)
Alicante
Cartagena
EXPERIMENTAL RESULTS

## Slide 36
9
LOSSLESS COMPRESSION (entropy-based evaluation)
Alicante
Cartagena
EXPERIMENTAL RESULTS

## Slide 37
9
LOSSLESS COMPRESSION (entropy-based evaluation)
Alicante
Cartagena
EXPERIMENTAL RESULTS

## Slide 38
10
LOSSY COMPRESSION (entropy-based evaluation)
EXPERIMENTAL RESULTS
Alicante
Cartagena
UPLINK BIT BUDGET: 2 bps
UPLINK BIT BUDGET: 1 bps

## Slide 39
10
LOSSY COMPRESSION (entropy-based evaluation)
EXPERIMENTAL RESULTS
Alicante
Cartagena
UPLINK BIT BUDGET: 2 bps
UPLINK BIT BUDGET: 1 bps

## Slide 40
10
LOSSY COMPRESSION (entropy-based evaluation)
EXPERIMENTAL RESULTS
Alicante
Cartagena
UPLINK BIT BUDGET: 2 bps
UPLINK BIT BUDGET: 1 bps

## Slide 41
CONCLUSIONS
TABLE OF CONTENTS
INTRODUCTION
DUAL LINK IMAGE CODING
EXPERIMENTAL RESULTS
Earth Obervation (EO) satellites in geosynchronous orbits have limited download capacity
Imaging sensors in EO satellites have increased their resolution
Need to trim down data before it is downloaded
Research purpose: increase the download capacity of EO satellites
  Motivation

## Slide 42
11
CONCLUSIONS
Earth Obervation (EO) satellites in geosynchronous orbits have limited download capacity
Imaging sensors in EO satellites have increased their resolution
Need to trim down data before it is downloaded
Research purpose: increase the download capacity of EO satellites
  Motivation
Exploit the temporal redundancy of satellite data
Use the uplink of the satellite, which is otherwise idle during transmission time
  Insights
  Dual link image coding
Lossless coding performance: gains about 0.5 to 1 bits per sample (bps)
Lossy coding performance: gains about 5 to 10 dB at low rates
  Experimental results (based on the data entropy)
  Traditional approach

## Slide 43
11
CONCLUSIONS
Earth Obervation (EO) satellites in geosynchronous orbits have limited download capacity
Imaging sensors in EO satellites have increased their resolution
Need to trim down data before it is downloaded
Research purpose: increase the download capacity of EO satellites
  Motivation
Exploit the temporal redundancy of satellite data
Use the uplink of the satellite, which is otherwise idle during transmission time
  Insights
  Dual link image coding
Lossless coding performance: gains about 0.5 to 1 bits per sample (bps)
Lossy coding performance: gains about 5 to 10 dB at low rates
  Experimental results (based on the data entropy)
  Traditional approach

## Slide 44
11
CONCLUSIONS
Earth Obervation (EO) satellites in geosynchronous orbits have limited download capacity
Imaging sensors in EO satellites have increased their resolution
Need to trim down data before it is downloaded
Research purpose: increase the download capacity of EO satellites
  Motivation
Exploit the temporal redundancy of satellite data
Use the uplink of the satellite, which is otherwise idle during transmission time
  Insights
  Dual link image coding
Lossless coding performance: gains about 0.5 to 1 bits per sample (bps)
Lossy coding performance: gains about 5 to 10 dB at low rates
  Experimental results (based on the data entropy)
  Traditional approach